## Slide 1
SELECTED LAYOUT · 6 × 40 m
75,000 t/yr MSW · SH-01 → 80 mm trommel → SH-03 on overs · magnets · 6 × 40 m tunnels · output by truck to FCG
SELECTED LAYOUT · INTERIM
30.0%
MASS REDUCTION
75,000 → 52,485 t/yr
80 mm
TROMMEL TR-01
65% unders · 35% to SH-03
4 × 343 m³
DETECTION BAYS
12 h hold · peak 481 t
40 /wk
TRUCKS TO FCG
13.5 per unload · ~16 min each
4.46 m
FILL IN EVERY TUNNEL
481 t per load · 40 m
26029-PFD-003 rev D · Coleraine / Riverridge · WTT 26029 rev 1 basis · sheet 1 of 3
Notes: Rev C adds preprocessing: SH-01 primary shredder, M1, TR-01 80 mm trommel. Unders (65%, assumed) go via M2 to the detection bays; overs (35%) go via M3 to the SH-03 secondary shredder (about 16.3 t/h) and M4, then to the bays. Blazequel on both shredder outfeeds. M5 sits on the SP-01 output line. Tunnel figures keep WTT's 75,000 t basis; ferrous removal makes them about 1.2% conservative.

## Slide 2
DAILY RHYTHM · MON–SAT
Loading in the morning, shredding and screening in the afternoon, so the two never share a bay.
SELECTED LAYOUT · INTERIM
06:00
08:00
10:00
12:00
14:00
16:00
18:00
20:00
L1 · Mon/Wed/Fri
② turn T1→T4 · 122 b
L2 · Mon/Wed/Fri
① empty T4 → trucks → FCG · 107 b
feed SH-01
L1 · Tue/Thu/Sat
③ fill T1 from bay pairs A + B · 153 b
L2 · Tue/Thu/Sat
feed SH-01
SH-01 → TR-01 → SH-03
shred · screen 80 mm · overs re-shred → bays
SH-02 bulky
bulky 4.8 h/day
Detection bays
IR cameras + auto deluge, 24/7
13.9 h
last shred 17:08 → next fill 07:00
≥ 12 h hold on every load (max 66 h over the weekend)
16.3 t/h
SH-03 on trommel overs
26,047 t/yr in the same 1,600 h as SH-01
~2,790 h
loader-hours a year
2 loaders, both under 1,600 h (no hopper feed)
26029-PFD-003 rev D · Coleraine / Riverridge · WTT 26029 rev 1 basis · sheet 2 of 3
Notes: Shown for the 7 + 7 process with a turn. In single-pass 14-day mode, loads are Tue/Thu/Fri and unloads Mon/Wed/Thu (see the dashboard and the rotation page). Bucket counts at 9 m³ and an assumed 2-minute cycle.

## Slide 3
STREAM TABLE & OPEN ITEMS
Annual averages, WTT 26029 rev 1 basis. MSW check: output 52,485 + off-gas 15,090 + 7,425 = 75,000 t/yr.
SELECTED LAYOUT · INTERIM
No. | Stream | t/yr | DS %
1 | MSW delivered | 75,000 | 63.0
3 | MSW to SH-01 primary (no picking) | 75,000 | 63.0
3a | SH-01 → M1 → TR-01 trommel 80 mm | 74,419 | –
4a | Unders <80 mm (65%) → M2 → bays | 48,295 | –
4b | Overs >80 mm (35%) → M3 → SH-03 → M4 → bays | 25,836 | –
4 | To detection bays (WTT basis kept) | 75,000 | 63.0
6 | Off-gas, first 7 days (water + degradation) | 15,090 | –
7 | Turn → second 7 days | 59,910 | 75.4
8 | Off-gas, second 7 days (incl. heat evap.) | 7,425 | –
10 | Tunnel output → trucks → FCG (40 /wk) | 52,485 | 84.6
16 | Ferrous recovered M1–M4 (1.29% Fe) | 869 | –
11 | Bulky → SH-02 → off-site | 60,000 | –
DESIGN CHOICES
6 identical 40 m tunnels, 481 t at 4.46 m
SH-01 → 80 mm trommel; overs via SH-03
Magnets M1–M4 (M5 TBC); Blazequel on both shredders
4 IR-watched bays, 12 h hold
Output straight onto trucks to FCG
STILL TO CONFIRM
Trommel unders split (65% assumed)
Magnet efficiencies (assumed)
Truck booking + set-down area for FCG loads
WTT: 40 m stage 2 heat / single pass
NIEA / NIFRS pile limit and fire water
26029-PFD-003 rev D · Coleraine / Riverridge · WTT 26029 rev 1 basis · sheet 3 of 3
Notes: Streams 3a, 4a, 4b and 16 are new in rev C. Tunnel streams keep WTT's 75,000 t basis even though ~870 t of ferrous is removed before the tunnels (about 1.2% conservative). m³ at 350 kg/m³.